## Slide 1
TDMA Network Schedule Planner & Optimizer
Wireless Protocol Development Technical Internship Challenge
Vaan Megam Networks Private Limited (VMN), Chennai
STUDENT PRESENTER DETAILS
• Name: Kamal Vigneshwaraa S
• Department: Information Technology
• College: Sri Sairam Institute of Technology, Chennai
• Domain: Wireless Protocol Development & Graph Optimization

## Slide 2
1. Executive Summary & Solution Workflow
1. Shared Spectrum
Radio signals collide without scheduling.
2. Graph Brain
Builds physical & conflict graphs.
3. DSATUR Engine
Colors conflict graph to optimize slots.
4. EMANE Profile
Generates XML profiles for emulator.
Core Project Deliverables & Approach
• Part 1 (Network Brain): Software engine using graph theory and distance-2 coloring for conflict-free scheduling.
• Spatial Reuse Optimization: Maximize simultaneous non-interfering transmissions to minimize frame length.
• Part 2 (Physical Emulator Bridge): Convert calculated schedule matrix into native EMANE TDMA Radio Model profiles.
• Verification & Containerization: 100% collision-free verification and Docker container deployment.

## Slide 3
2. Core Wireless Concepts — TDMA Workflow
1. Frame Init
Time divided into recurring frames.
2. Slot Allocation
Discrete 1ms slots assigned per node.
3. Exclusive Tx
Node transmits exclusively in slot.
4. Clean Reception
Receivers receive uncorrupted data.
Key Operational Principles
• Shared Radio Frequency: Multiple radio nodes communicate over the exact same frequency channel by sharing time.
• Synchronized Time-Slots: Discrete, synchronized time-slots prevent simultaneous transmissions by adjacent radios.
• Zero Receiver Collisions: Correct scheduling guarantees zero signal overlapping and clean packet delivery.
• Clock Synchronization: All participating radios maintain tight clock sync for precise slot timing boundaries.

## Slide 4
3. Interference Classification Workflow
1. Radio Pair
Check node pair distance.
2. Dist <= 500m
1-Hop Direct Link (Distance-1).
3. Common Neighbor
2-Hop Hidden Terminal (Distance-2).
4. Slot Decision
Assign distinct timeslots!
Direct Link (Distance-1)
• Radios located directly within range (<= 500m).
• 1-Hop Neighbors in physical graph.
• Transmissions jam each other directly.
• MUST be assigned different time-slots.
Hidden Terminal (Distance-2)
• Radios transmitting to common receiver (A -> B <- C).
• 2-Hop Neighbors in physical graph.
• Signals collide at intermediate receiver B.
• MUST be assigned different time-slots.

## Slide 5
4. Spatial Reuse Decision Workflow
1. Distance Check
Shortest path distance > 2 hops.
2. Interference Check
Zero signal overlap at any receiver.
3. Slot Re-allocation
Safe timeslot reuse across nodes.
4. Capacity Boost
Dramatically increased network throughput!
Benefits of Spatial Reuse Optimization
• No Receiver Collision: Radios separated by > 2 hops cause zero signal interference at receivers.
• Frame Length Minimization: Reduces total unique time-slots required per frame (e.g. 16 nodes in 9 slots).
• Throughput Multiplication: Multiple radios transmit simultaneously in parallel across the network.
• NP-Hard Optimization: Calculates optimal spatial reuse using intelligent graph coloring heuristics.

## Slide 6
5. System Architecture & 5-Stage Processing Workflow
1. Stage 1: Input Data
Receives 2D coordinates for all radio nodes and configures radio range (500m).
2. Stage 2: Graph Build
Constructs Physical Graph G (1-hop links) & Distance-2 Conflict Graph G_conflict.
3. Stage 3: DSATUR Engine
Executes DSATUR graph coloring algorithm to assign non-conflicting slots.
4. Stage 4: Verification
Performs 100% collision verification check for all 1-hop and 2-hop neighbor pairs.
5. Stage 5: EMANE Bridge
Translates schedule matrix into native EMANE XML configuration profiles.

## Slide 7
6. Part 1 — DSATUR Graph Coloring Workflow
1. Build G_conflict
Add edge if shortest path is 1 or 2 hops.
2. Track Saturation
Count neighbor assigned colors.
3. Pick Max Priority
Select uncolored node with max saturation.
4. Assign Color
Assign lowest valid integer color index.
Mathematical Graph Coloring Principles
• Physical Graph G = (V, E): Vertices represent radios, edges represent 1-hop physical links (<= 500m).
• Conflict Graph G_conflict: Edge added if path is 1 or 2 hops. Nodes > 2 hops share no edge (allows spatial reuse).
• Saturation Degree Metric: Dynamic priority metric tracking number of distinct colors assigned to neighbors.
• Lowest Valid Color: Assigns lowest integer color index {0, 1, 2, ...} not used by neighbors in G_conflict.

## Slide 8
7. Part 1 — Verification & Report Workflow
1. Exhaustive Pair Check
Check all 1-hop & 2-hop pairs.
2. Collision Freedom
Confirm zero shared timeslots.
3. Frame Optimization
Verify minimal frame length.
4. Matrix Output
Generate Slot x Node Boolean matrix.
Verification Engine Outcomes
• 100% Conflict-Free Verification: Exhaustively verifies all 1-hop and 2-hop node pairs across topology.
• Zero Receiver Collisions: Guarantees zero direct link and zero hidden terminal collisions.
• Optimized Frame Length: Reduces 16-node grid frame length down to 9 unique timeslots.
• Structural Matrix Representation: Produces formatted Slot x Node Boolean schedule matrix representation.
• Clean Execution Status: Reports confirmation: Execution finalized cleanly. Schedule verified conflict-free.

## Slide 9
8. Part 2 — EMANE Integration Workflow
1. Schedule Matrix
Receive Python calculated slots.
2. XML Profile Generator
Create 1ms slots & NEM tx mapping.
3. Multicast Event Bridge
Publish events to EMANE daemon.
4. Docker Container
Single-command deployment setup.
EMANE Emulation Integration Details
• EMANE Emulation Framework: Extendable Mobile Ad-hoc Network Emulator for real-time wireless protocol testing.
• Native Profile Generation: Translates node-to-slot mapping into native XML schedule profiles.
• 1ms Slot & NEM Mapping: Configures 1ms slot duration, 1MHz bandwidth, 2.4GHz frequency, per-NEM slots.
• Multicast Event Publisher: Broadcasts schedule updates to EMANE event daemons over UDP multicast.
• Docker Containerization: Consolidated Dockerfile & Docker Compose configuration for containerized deployment.

## Slide 10
9. Conclusion & Project Outcomes
1. Math Optimization
Graph coloring with spatial reuse.
2. Zero Collisions
Distance-1 & Distance-2 eliminated.
3. EMANE Integration
Native XML profiles generated.
4. Real Deployment
Applicable to 5G & MANET tactical networks.
Summary of Achievements & Impact
• Complete Solution: Successfully solved both Part 1 (Network Brain Engine) and Part 2 (EMANE Physical Emulator Bridge).
• Mathematical Collision Freedom: Eliminated direct link and hidden terminal collisions completely.
• Optimal Spatial Reuse: Maximized parallel non-interfering transmissions, reducing total frame length.
• Standardized Output: Seamless integration with EMANE emulation environment.
• Real-World Application: Directly applicable to 5G private networks, MANET tactical communications, and SDR mesh networks.